LoRa Fabian Shield wiki

## Reset :
There is a Reset button on the board. We linked the reset to the Arduino reset. This way, full system (shield + Arduino) is reseted when you press the button.

Note that the reverse is not true. When you press the Arduino Reset button, the shield doesn't reset. There is a voltage level shifter between the two boards. This component is unidirectional and it is routed from the shield to the Arduino. (To be confirmed on the V2)

If you don't like this behavior of Reset lines connected and you want to keep the two reset functions independent, you can remove resistor R129 on the shield. This way you will be able to reset either the shield or the Arduino independently.

## Ceramic Antenna:

To reduce price and size of the shield we choose a ceramic antenna. Performance can be good with it but you have to take care of antenna orientation regarding the peer device.

Here is the radiation pattern from the antenna data sheet:

As you can see, there is direction in which the antenna have bad performances, so you should take care of the orientation you choose for your device.

The easiest way to find a good position for your device is experimentation. Try different positions and see which one gives you the best results.

## Radio propagation :
You have to be aware that Radio link quality and performances are highly dependent of environment.

Better performances can be reached with:
- Open air environment.
- No obstacles.
- No radio interferer is the ISM 868MHz band.
=> In this conditions it is possible to achieve good qualities communications on several kilometers.

Radio performances are degraded with:
- Obstacles: buildings, trees...
- Inner buildings environments.
- High ISM 868MHz band usage by other technologies.

Radio communication are usually killed with bad topographic conditions. It is usually not possible
to communicate through a hill, even very small.